## Slide 1: ELECTROCHEMISTRY
EXTRACTION OF ALUMINIUM

## Slide 2: What is Aluminium Ore called?
Aluminium ore is called bauxite.
What is the Chemical Formula for Aluminium Oxide?
Al2O3.

## Slide 4: Extraction of Aluminium
Aluminium cannot be extracted from their oxides by reduction with carbon because:
It is more reactive than carbon, so the reaction does not work.
Instead, it is extracted by electrolysis. The ore is first converted into pure Aluminium oxide by the Bayer Process (involves treatment with sodium hydroxide solution, and this is then electrolysed in solution in molten cryolite - another Aluminium compound.

## Slide 5: Bayer Process
Bauxite, Al2O3.2H2O contains iron oxides, silicon dioxide and titanium dioxide as impurities
First roasted in air to convert iron(II) compounds to iron(III) compounds
Heated at 160ºC under pressure up to 35atm with NaOH(aq)
  Al2O3(s) + 6OH-(aq) + 3H2O(l)  2[Al(OH)6]3-(aq)
Undissolved impurities filtered off – ‘red mud’
Remaining liquid ‘seeded’ with aluminium hydroxide
Hydrated alumina (aluminium oxide) percipitates
  2[Al(OH)6]3-(aq)  Al2O3.3H2O(s) + 6OH-(aq)
Percipitate is filtered , washed, dried and heated to give pure aluminium oxide, Al2O3, a white powder

## Slide 6: Extraction of Aluminium

## Slide 7: Extraction of Aluminium
The aluminum oxide must be in molten
Aluminium oxide has a very high melting point : 2040ºC
Cryolite Na3AlF6 added to:
  Dissolve the aluminium oxide so that the melting point of the electrolyte is lowered to about 970ºC
  Improve the electrical conductivity of the electrolyte
When a current of 12 000A at a voltage of 5V is applied,
  Al3+ is attracted to the cathode (negative electrode)
  O2- is attracted to the anode (positive electrode)

## Slide 8: Half-Equation
At the cathode,
  Al3+ gains 3 electrons at the cathode and are reduced to aluminium atoms
  Al3+(l) + 3e-  Al (l)
  The denser Al drops to the bottom of the cell and removed using a suction tube or through a tap hole
At the anode,
  O2- loses 2 electrons at the anode and are oxidised to form oxygen
  2O2-(l)  O2(g) + 4e-
  Oxygen reacts with hot carbon electrodes to give CO2 gas. Thus, the electrodes have to be replaced periodically

## Slide 9: Overall Equation
4Al3+ + 12e-  4Al
6O2-  3O2 + 12e-
Overall equation:
  4Al3+ + 6O2-  4Al + 3O2
  Or
  2Al2O3  4Al + 3O2

## Slide 11: Aluminium
Aluminium is especially useful because it
has a low density;
is strong when alloyed;
is a good conductor of electricity;
has a good appearance;
resists corrosion because of the strong thin layer of aluminium oxide on its surface.
Aluminium is used for aircraft, trains, overhead power cables, saucepans and cooking foil

## Slide 12: Uses of Aluminium
Uses | Properties
Overhead electric cables | Low density, Light Resistant to corrosion Good electrical conductivity
Food containers | Non-toxic Resistant to corrosion Light
Aircraft body | Low density Light High tensile strength Resistant to corrosion
Saucepans | Light Resists corrosion Good appearance Good conductor of heat

## Slide 13: PAST YEAR QUESTIONS MAY / JUNE 2002

## Slide 15: THE END THANK YOU :D